## Slide 1: ICS 3103 Data communications lecture Signal-to-Noise Power Ratio
Prof.Cheruiyot w.k,
JKUAT-ICSIT
Computing Department

## Slide 2: Signals and noise
One of the fundamental problems in signal measurement is distinguishing the noise from the signal.
It is not always easy.
The signal is the "important" part of the data that you want to measure - it might be the average of the signal over a certain time period, or it might be the height of a peak or the area under a peak that occurs in the data.

## Slide 3: Sources of noise
Building vibrations, air currents, electric power fluctuations, stray radiation from nearby electrical equipment, static electricity, interference from radio and TV transmissions, turbulence in the flow of gases or liquids, random thermal motion of molecules, background radiation from natural radioactive elements, "cosmic rays" from outer space (seriously), and even the basic quantum nature of matter and energy itself, etc

## Slide 4: Signal-to-noise ratio
The quality of a signal is often expressed quantitatively as the signal-to-noise ratio (SNR), which is the ratio of the true signal amplitude (e.g. the average amplitude or the peak height) to the standard deviation of the noise.
SNR measurement describes how much noise is in the output of a device, in relation to the signal level.
Measuring the signal-to-noise ratio is much easier if the noise can be measured separately, in the absence of signal.

## Slide 5: Signal-to-noise ratio
Every device has some amount of noise at its output.
A small amount of noise may not be objectionable if the output signal is very strong.
In many cases, the noise may not be audible at all. But if the signal level is very small, even a very low noise level can have an adverse effect.

## Slide 6: Basics
Signal-to-noise ratio (SNR or S/N) is a measure used in science and engineering that compares the level of a desired signal to the level of background noise.
It is defined as the ratio of signal power to the noise power, often expressed in decibels.
A ratio higher than 1:1 (greater than 0 dB) indicates more signal than noise.
While SNR is commonly quoted for electrical signals, it can be applied to any form of signal (such as isotope levels in an ice core or biochemical signaling between cells).

## Slide 7: Basics
The signal-to-noise ratio, the bandwidth, and the channel capacity of a communication channel are connected by the Shannon–Hartley theorem.
Signal-to-noise ratio is sometimes used informally to refer to the ratio of useful information to false or irrelevant data in a conversation or exchange. For example, in online discussion forums and other online communities, off-topic posts and spam are regarded as "noise" that interferes with the "signal" of appropriate discussion.

## Slide 8: Definition
Signal-to-noise ratio is defined as the power ratio between a signal (meaningful information) and the background noise (unwanted signal):
    where P is average power.
Both signal and noise power must be measured at the same or equivalent points in a system, and within the same system bandwidth.

## Slide 9
If the signal and the noise are measured across the same impedance (a constant related to electromagnetic wave propagation in a medium), then the SNR can be obtained by calculating the square of the amplitude ratio:
where A is root mean square (RMS) amplitude (for example, RMS voltage).
Because many signals have a very wide dynamic range, SNRs are often expressed using the logarithmic decibel scale.

## Slide 10: In decibels
In decibels, the SNR is defined as
which may equivalently be written using amplitude ratios as:

## Slide 11: For engineers…
Engineers frequently express SNR in decibels as
      Ps=signal power
      PN=noise power
Engineers consider a SNR of 2 (3 dB) to be the boundary between low and high SNRs.
In image processing, PSNR must be greater than about 20 dB to be considered a high-quality picture.

## Slide 12
The concepts of signal-to-noise ratio and dynamic range are closely related.
Dynamic range measures the ratio between the strongest un-distorted signal on a channel and the minimum discernable signal, which for most purposes is the noise level.
SNR measures the ratio between an arbitrary signal level (not necessarily the most powerful signal possible) and noise.
Measuring signal-to-noise ratios requires the selection of a representative or reference signal.

## Slide 13
In audio engineering, the reference signal is usually a sine wave at a standardized nominal or alignment level, such as 1 kHz at +4 dBu
SNR is usually taken to indicate an average signal-to-noise ratio, as it is possible that (near) instantaneous signal-to-noise ratios will be considerably different.
The concept can be understood as normalizing the noise level to 1 (0 dB) and measuring how far the signal 'stands out'.

## Slide 14
An alternative definition of SNR is as the reciprocal of the coefficient of variation, i.e., the ratio of mean to standard deviation of a signal or measurement:
      μ is the signal mean or expected value and
      δ is the standard deviation of the noise, or an estimate thereof.
The definition is most commonly used in image processing, where the SNR of an image is usually calculated as the ratio of the mean pixel value to the standard deviation of the pixel values over a given neighborhood.

## Slide 15: Improving SNR in practice
All real measurements are disturbed by noise. This includes electronic noise, but can also include external events that affect the measured phenomenon — wind, vibrations, gravitational attraction of the moon, variations of temperature, variations of humidity, etc., depending on what is measured and of the sensitivity of the device.
It is often possible to reduce the noise by controlling the environment. Otherwise, when the characteristics of the noise are known and are different from the signals, it is possible to filter it or to process the signal.

## Slide 16: Interference
Most definitions implicitly assume that the signal and the noise are statistically unrelated and arise from different sources.
In many applications, some part of what is not signal arises from man-made sources and can be statistically related to the signal. For example, a cellular telephone's signal can be corrupted by other telephone signals as well as noise.
Such non-signals are termed interference and a signal-to-interference ratio, abbreviated SIR
However, when both interference and noise are present, neither the SIR nor the SNR characterizes the performance of signal processing systems.

## Slide 17
For example, it is sometimes possible to modulate and confine the signal within a very narrow bandwidth and then filter the detected signal to the narrow band where it resides, thereby eliminating most of the broadband noise. When the signal is constant or periodic and the noise is random, it is possible to enhance the SNR by averaging the measurement. In this case the noise goes down as the square root of the number of averaged samples.